The project presents an drone coordination system featuring an integration between a P4-programmed server and a Python-based client using Scapy for packet crafting and network interactions.
Server-Side The server component, implemented in P4, handles packet processing for drone control communications. It is tailored to interpret custom drone protocol headers and manage multiple operational aspects:
- Collision Detection: Utilizes a system of registers to store and retrieve current positions of drones, actively checking for potential overlaps or conflicts before approving movement commands.
- Broadcast System: Manages a communication protocol among drones, allowing each unit to broadcast its current position which is then captured and processed by other drones within the network.
- Command Execution: Based on parsed packet data, the server executes movement commands like forward, backward, left, and right, adjusting drone positions accordingly and considering spatial constraints to prevent collisions.

What I have learned:
I have learned to utilised header of the sent packet to create custom protocol, parse it and handled it on a P4 environment. I gain expertise when overcoming the challenge and constraint in P4, such as create pseudo loop and register. Bitwise operation offered me insight to how I can handle a switch like a microcontroller, which is useful when setting flag etc.

A test with 3 drones was conducted, which were controlled by three separate client scripts. The
collision detection function and broadcasting system function normally

The code: https://github.com/Sitaoooo/CWM-ProgNets/tree/f0b364cee2e9a2c8dd24fc1bec46d212d5eb448a/scripts